## Slide 1: Special Features of LAN8670/1/2 and LAN8650/1
June 2024

## Slide 2: Agenda
LAN8670/1/2 and LAN8650/1 Review
Features to Tune Bandwidth
Supporting Time Sensitive Networking
Wake/Sleep

## Slide 3: What is 10BASE-T1S?
IEEE 802.3-2022
Ethernet over a balanced pair of conductors
10 Mbps shared
Half duplex multidrop bus line with PLCA
Up to at least 8 nodes*
Up to at least 25m bus length*
        *AN1829 demonstrates up to 50 nodes and 100 meters
ECU
Sensor
Sensor
Sensor
Sensor
Notes: Let’s come to the question: what is 10BASE-T1S ?
It is a technology to connect Ethernet devices using a balance pair of connectors as a bus line.
10BASE-T1S supports a bandwidth of 10 megabits per second on a shared connection.
On a bus line, it uses half-duplex data transmission,
Up to at least 8 nodes, depending on the environment and cableing, can be connected via a multidrop bus.
The bus length can go up from a few cm to at least 25m, and even higher.
Alternatively, on a point-to-point connection, the 10BASE-T1S standard specifies a half-duplex or full-duplex mode, with up to 15m connection length.
The technology is being developed as the IEEE 802.3cg standard,
which envisions low power physical layer transceivers
and a bus line connection without collisions.
10BASE-T1S supports AEC-Q100 Temperature Grade 1 and
Functional Safety requirements, as needed for high-reliability applications.

## Slide 4: System Block Diagram - LAN8670/1/2 Family
10BASE-T1S bus
MCU
LAN8670/1/2
MII/RMII
Sensors &
Actuators
Switch
LAN8670/1/2
MII/RMII
MAC
100/1000BASE-TX
Notes: The LAN8670/1/2 is a high-performance 10BASE-T1S single-pair Ethernet PHY transceiver for 10 Mbit/s halfduplex networking over a single pair of conductors, designed according to the IEEE Std 802.3cg-2019™.
The LAN8670/1/2 connects via an MII or RMII interface to an Ethernet MAC Layer, running on an external MCU. The LAN8670/1/2 can be configured via a standard SMI-interface by the external MCU, and connects to the 10BASE-T1S network using 2 differential pins.
The MCU itself may be connected to several sensors or actuators, collecting and processing their data, or may be connected to any other application.
Similarly, the LAN8670/1/2 may be connected via MII or RMII to an Ethernet switch application which passes the data to/from the 10BASE-T1S network to other network segments having higher speed.

## Slide 5: LAN8650/1 MAC-PHY
SPI Interface, 5 pins
  OA TC6 V1.1 SPI specification
Works with almost all MCUs
LAN8650: Requires 3.3 and 1.8V supplies
LAN8651: Single 3.3V supply with integrated 1.8V regulator
MAC-PHY
MAC
Digital PHY
Analog PHY
MCU
SPI
MCU
PHY
Digital PHY
Analog PHY
MII
RMII
MAC
Notes: The LAN8650/1 is a high-performance 10BASE-T1S MAC-PHY for 10 Mbit/s halfduplex networking over a single pair of conductors, designed according to the IEEE Std 802.3cg-2019™.
The LAN8650/1 connects via an SPI interface to an external MCU. The LAN8650/1 can as well be configured via the SPI interface by the external MCU, and connects to the 10BASE-T1S network using 2 differential pins.
The MCU itself may be connected to several sensors or actuators, collecting and processing their data, or may be connected to any other application.

## Slide 6: References
10BASE-T1S,
PLCA,
Live Demo using MCHP Eval Boards,
Analysis of Network Bandwidth
10base-t1s-single-pair-ethernet-system-integration
~1 hour
&
Presentation

## Slide 7: Agenda
LAN8670/1/2 and LAN8650/1 Review
Features to Tune Bandwidth
Supporting Time Sensitive Networking
Wake/Sleep

## Slide 8: PLCA - Basics
Organize Media Access
Physical Layer Collision Avoidance
(PLCA) IEEE 802.3cg
0
1
2
3
4
Unique Node IDs
Notes: The key is to avoid physical collisions by organizing the media access,
This IEEE standard is called Physical layer collision avoidance, or just PLCA in short.
One of the basics for PLCA is that each node has its unique NodeID, but the order of the Ids in the network is not relevant.

## Slide 9: PLCA - Basics
0
1
2
N
…
3
Round Robin
Notes: Transmit opportunities are given in a round robin manner to each node.
And only the node that owns a certain transmit opportunity is allowed to send its data .
This rule avoids collisions on the bus line.

## Slide 10: PLCA - Basics
BEACON
PLCA Coordinator
Node-0
PLCA Bus Cycle
TO-2
TO-0
…
B
TO-0
TO-1
TO-N
B
0
0
0
0
0
0
0
TO-1
TO-N
0
Transmit Opportunity (TO) of Node N
Silence
TO from
PLCA Follower
Node-1,2...N
time
Notes: Every transmit opportunity is followed by a short silence to make sure that all nodes have recognized the beginning of the next transmit opportunity .
Once all transmit opportunities have passed, this is called a PLCA bus cycle.
A new PLCA bus cycle is started right away by sending out a beacon signal from the PLCA coordinator device which is node zero.
All other devices, called PLCA-Followers, synchronize their internal timings to this BEACON, to know when their TO starts.

## Slide 11: Increasing Node Bandwidth
Burst
Multiple Transmit Opportunities

## Slide 12: Burst Mode
3 frames in TO-1
Max Burst Count = 2 (additional frames)
TO-5
B
0
2
3
TO-1: #1
TO-4
B
…
…
TO-1: #2
TO-1: #3
5
No Silence
Silence
3 x more frames
per cycle
Notes: Burst Mode is feature of PLCA , to enhance the bandwidth which can be used by a specific node.
In this example Node-1 can send three Ethernet frames (the yellow ones) without interruption in the same TO. The node just needs to be configured with a Maximum Burst Count setting of 2, and that means 2 additional frames.
As a result, Node-1 can potentially send 3 times as many frames per cycle compared to the other nodes.
Note that there is no silence between the frames of a burst, but at the end of the 3 frames.

## Slide 13: Controlling Burst: PLCA_BURST Register
This feature is described in the IEEE standard, but the registers are not. All PHYs have this feature.
Max burst count
= number of add. frames per TO
Burst timer
= max time between two frames of the burst
LAN8670/1/2: MMD 0x1F
LAN8650/1: MMS4

## Slide 14: Multiple Transmit Opportunities / Node IDs Example
Node_Ids #1, #3, #5
Assigned to same device
No need to wait for next bus-cycle
TO-5
B
0
TO-1
TO-5
B
…
…
TO-2
TO-3
TO-4
ID=0
ID=2
ID = 1
ID1 = 3
ID2 = 5
ID=4
Reduced latency,
more bandwidth
for this node
Notes: Assigning Multiple NodeIDs to a single node is an advanced feature of the LAN867x and LAN865x, to enhance the latency and bandwidth for a specific node.
In the example one of the devices has been assigned the three nodeIDs, #1, #3 and #5 (the yellow ones).
After the transmission in TO-1, followed by a short silence, the TO-2 is used by some other device. However, our local device can use already TO-3 for its next frame, instead of waiting for a full PLCA bus-cycle. This reduces the latency for the local device, even if TO-0, 2, and 4 are used by other devices. Also the available bandwidth for the local device increases.

## Slide 15: Controlling Multiple Transmit Opportunities
LAN8670/1/2: MMD 0x1F
LAN8650/1: MMS4
Additional TOs
(up to 8)
This feature is unique to Microchip PHYs. It work with on a bus with any standard compliant PHYs.

## Slide 16: Decreasing Node Bandwidth
Transmit Opportunity Skipping
Credit Based Shaper

## Slide 17: Transmit Opportunity Skipping
If a node does not transmit often, it can be configured to ignore a set number of TOs after each packet it transmits.
  This is only useful it a low bandwidth node has bursty, non-time critical data.
Notes: It is almost always possible to adjust bandwidth by giving some nodes more bandwidth using either Burst or Multiple Transmit Opportunities. Given that Ethernet won‘t try to transmit if it doesn‘t have something, it is rare to need to reduce bandwidth. The easiest ways to reduce bandwidth is transmit opportunity skipping.

## Slide 18: Controlling Transmit Opportunity Skipping
Configure the number of TOs to skip before enabling the mode
This feature is not in the standard but is found in other PHYs (the control registers will be different). It work with on a bus with any standard compliant PHYs.
LAN8670/1/2: MMD 0x1F
LAN8650/1: MMS4
Number of TOs
to Skip
TO Skipping
Enable

## Slide 19: CBS – Credit Based Traffic Shaping
Provides a node a certain bandwidth based on credits.
  Prevents a “best-effort-node” from flooding the network
  This is NOT MAC-based traffic shaping – there are no queues
Bandwidth distribution independent of Ethernet frame length
HW-based: Application only needs to configure
Do not mix with PLCA Burst Mode
Does not require PLCA (functions in CSMA/CD mode)
This feature is unique to Microchip PHYs. It work with on a bus with any standard compliant PHYs.
Enables
traffic shaping in small MCUs
Notes: The LAN8670/1/2 and LAN8650/1 implements a hardware credit based traffic shaper (CBS) to control the station’s transmit bandwidth. A hardware credit counter is used to enable and disable the ability to transmit packets onto the medium. The PHY decrements the credit counter during transmit and increments the counter when the PHY is receiving data or the medium is idle. When the credit counter is below the stop threshold, the PHY does not have enough credits to begin transmitting a packet, however it will complete the current packet, regardless of length. Once below the threshold and no longer transmittion, the PHY will then hold the MAC off from transmitting by asserting carrier sense (creating a logical collision). When the PHY is not transmitting, it will accumulate credits. Once the credit counter exceeds the start threshold, carrier sense will operate normally.
The CBS is harder to debug and configure than transmit opportunity skipping. Nodes cannot use burst mode (so that may need to be disabled in a driver).
Because PLCA uses bandwidth more efficiently than CSMA/CD, CSMA/CD should only be used during start-up or error recovery. During these phases, there is no need for bandwidth control.

## Slide 20
Credit Based Traffic Shaping
LAN8670/1/2
&
LAN8650/1
No more increment when
credits > TOPLIMIT
prevents bursts of packets
PHY starts TX only if
credits > STARTTHR
PHY stops TX when
credits < STOPTHR
Packet sent completely,
even when
credits < STOPTHR
No more decrement when
credits < BOTLIMIT
prevents waiting for too long
RISESLP (Rising Slope)
30 Bytes RX or 800 ms idle => +1 Credit
ECCRDS (empty Cycle Credits)
1 empty PLCA cycle
=> +30 Credits
FALLSLP (Falling Slope)
2 Bytes TX
=> -1 Credit
Notes: The PHY can only start transmitting when its credits are higher than the start threshold. Once the PHY allows the MAC to begin transmitting a packet, the entire packet will be transmitted even if the credit counter decrements below the stop threshold while it is transmitting.
The Falling Slope (FALLSLP) field of the Credit Based Shaper Slope Control (CBSSLPCTL) register configures the rate at which the credit counter loses credits when transmitting. Similarly, the Rising Slope (RISESLP) field configures the rate at which the credit counter will accumulate credits when the medium is idle or the PHY is receiving data.
When PLCA is enabled, credits may additionally be accumulated at an accelerated rate when no transmission is detected within each PLCA bus cycle. The rate at which credits are accumulated for each empty PLCA bus cycle is configured by the Empty Cycle Credits (ECCRDS) field.
The credit counter will saturate and stop accumulating credits when the limit set by the Top Limit (TOPLIMIT) field in the Credit Based Shaper Top Limit High/Low (CBSTPLMTH/CBSTPLMTL) registers is reached. Likewise, the credit counter will saturate and stop losing credits at the limit set by the Bottom Limit (BOTLIMIT) field. This prevents the credit counter from incrementing or decrementing into an overflow condition. The saturation of the credit counter also prevents the PHY from delaying transmission of a packet too long or transmitting a burst of packets. For example, the PHY may lose a significant number of credits by transmitting a maximal size packet. If the credit counter were not limited by a lower bound, it may take a significant amount of time for the PHY to accumulate enough credits to transmit another packet. Similarly, if the PHY has not transmitted in a long time, it may accumulate too many credits allowing it to transmit multiple frames if the credit counter were not limited by an upper bound. By controlling the top and bottom limits of the credit counter, the credit based shaper may be configured to transmit at the desired rate.

## Slide 21: Controlling CBS
Start Threshold: 20 bits
Stop Threshold: 20 bits
Slope Control: 8 bits each for FALLSLP and RISESLP
Top Limit: 20 bits
Bottom Limit: 20 bits
Current Credit Count: 20 bits
(Read-only – debug use)
Extra Increment for Empty Cycles
Enable Bit

## Slide 22: Summary of CBS Configuration
Less bandwidth available for certain nodes:
  Start/stop threshold can be configured differently in each node
  Higher start threshold => node needs to wait longer for TX
  Higher stop threshold => node needs to stop earlier when TX

## Slide 23: Time Division Multiplexing
ACMA

## Slide 24: Reminder: PLCA Bus Cycle
BEACON
PLCA Coordinator
Node-0
PLCA Bus Cycle
TO-2
TO-0
…
B
TO-0
TO-1
TO-N
B
0
0
0
0
0
0
0
TO-1
TO-N
0
Transmit Opportunity (TO) of Node N
Silence
TO from
PLCA Follower
Node-1,2...N
time
Notes: Every transmit opportunity is followed by a short silence to make sure that all nodes have recognized the beginning of the next transmit opportunity .
Once all transmit opportunities have passed, this is called a PLCA bus cycle.
A new PLCA bus cycle is started right away by sending out a beacon signal from the PLCA coordinator device which is node zero.
All other devices, called PLCA-Followers, synchronize their internal timings to this BEACON, to know when their TO starts.

## Slide 25: Application Controlled Multiple Access (ACMA)
ACMA Bus Cycle
Channel 2
…
Channel 0
Channel 1
Channel N
Channel 0
ACMA 1
…
ACMA 0
ACMA 0
ACMA 2
ACMA N
time
Notes: Each device can only begin transmission when its ACMA pin is asserted. ACMA is set for active high in this example.
Device 1 can start to transmit when ist ACMA input is high.
So can device 2.
And so on.
We see with device N, when it doesn‘t have something to transmit, it can still begin tranmitting any time that ACMA is asserted.
And it will transmit a complete packet, regardless of length. So the ACMA pulse timing must allow for the worst case packet length, plus some extra for jitter.
The ACMA pulses need to be synchronized, so you either need and external clock, or you need to run a clock sychronization algorithm. This take development effort, debug time, plus code and data memory and processor cycles.
For Watson, ACMA uses IO pins that may be better used for something else. If you are using ACMA, you need to make sure that you have a pin available for RXPI if you will be using PTP to synchronize your clock.
For Galileo, you can use the internal event generator 0 as a source for ACMA if you can synchronize the wall clock.

## Slide 26: Common Configuration
ACMAPOL =1 (ACMA Polarity)
in PINCTRL (Pin Control Register)
ACMAEN =1 (ACMA Enable)
in ACMACTL (ACMA Control Register)
Debugging:
UNCRS (Unexpected Carrier Sense)
in STS1 (Status1 Register) can
Be signaled via interrupt

## Slide 27: LAN8670 in RMII Mode
ACMA pin available
in each LAN867x variant
Sometimes muxed with other functions
RMII Interface
Dedicated ACMA pin available
in RMII / SC-MII mode, if enabled
Notes: The LAN8670 supports a dedicated ACMA pin in SC-MII mode and in RMII mode.

## Slide 28: LAN8650 ACMA
Internal or External Source
ACMASEL = 01 ACMA-signal by EG0 (Event Generator 0) internally passed to PHY
ACMASEL = 10 ACMA-signal input on DIOA2 from external MCU, passed to PHY
A2SEL = 00 ACMA-signal input from external MCU
A2SEL = 01 DIOA2 signal output from Event Generator 2
Or
it can be an external input from MCU into DIOA2 pin
ACMA-signal can either be generated internally
Miscellaneous Registers (MMS 10)

## Slide 29: Agenda
LAN8670/1/2 and LAN8650/1 Review
Features to Tune Bandwidth
Supporting Time Sensitive Networking
Wake/Sleep

## Slide 30: What is Time Synchronization
Notes: Time Synchronization enables all devices on a network to have a common time reference. This allows data to be sampled and events to occur at known times.
The reference can be several hops away provided the bridges between segments are time aware. All time aware endpoints can synchronize to the wallclock provided by the time aware bridge, which synchronizes to the grandmaster.
For any endpoint, we just need to look at how it gets ist clock from it‘s local clock source.

## Slide 31: Clock Synchronization
We need to match the clock in the sink to clock in the source
  And STAY matched
Both clocks increment based on local oscillators
  Oscillators are never exactly the same
  If the oscillators appear to match but there is a phase offset, the clocks are syntonized

## Slide 32: Possible Software Architecture
Periodically get updates from an external reference, use a servo control algorithm to minimize the error between the clock
This is not good enough – there will always be a processing delay!
Clock Servo
Algorithm
Local Wall Clock
Reference Clock
+
-
X

## Slide 33: Better Software Architecture
Periodic updates from an external reference, use a servo control algorithm to minimize the error by changing the amount the local clock is incremented every tick of the local oscillator.
  First time through – set the wallclock as on the previous slide
This architecture works!
Clock Servo
Algorithm
Local Wall Clock
Reference Clock
+
-
Increment (ns.subns)

## Slide 34: But LAN8650/1 Updates via SPI?
SYNC messages are sent very slowly (8 – 16 per second)
  At least 62.5 milliseconds between updates
  Receive timestamps are directly passed with the Ethernet data (no register reads).
  Clock servo will update 0 to 2 registers each SYNC
Even over SPI, the updates can be made in a timely manner
  Control accesses are interleaved with packet data
  @15MHz, SPI will handle the full Ethernet bandwidth
    There is room for the few control accesses.
Because only the INCREMENT registers change, a slow interface will work
  A clock servo for a faster system will probably need some adjustment

## Slide 35: How does the Clock Source Share It‘s Time?
The Precision Time Protocol contains messages to share the time from the clock source
  SYNC message is sent from the source. It timestamps exactly when the messsage is sent, TS.
  The follower captures a timestamp when it receives the SYNC message, TF.
  The source sends a FOLLOWUP message containing TS.
  The follower now has 2 timestamps:
    TS and TF

## Slide 36: What is the Real Time at the Follower?
If there were no propagation delay, then TF and TS would be the same.
Call the propagation delay TD. The error at the follower is:
  δ = TF – (TS + TD)
How to determine TD?
  For larger networks, the Pdelay_resp and Pdelay_followup messages from PTP can be used to exchange another set of timestamps.
    With all 4 timestamps, it is possible to calculate roundtrip delay.
  For 10BASE-T1S networks, the distance between nodes is known so the delay can be calculated and treated as a constant.

## Slide 37: LAN8650/1 Receive Timestamp Configuration
The standard software configuration will set the pattern matcher to trigger a timestamp on ALL incoming packets.
  First 3 writes configure a timestamp to be taken at the end of the SFD (Source Frame Delimiter) symbol in the Ethernet frame based on the internal wall clock
  Last write enables the signal which triggers the timestamp

## Slide 38: LAN8650/1 Wall Clock Registers
To set the wall clock (used once at the start of the clock servo)
  MAC_TSH, MAC_TSL (48 bits of seconds)
  MAC_TSN (30 bits of nanoseconds)
To set the amount the wall clock is incremented each tick of the local osillator
  MAC_TI (8 bits of nanosecond adjustment)
  MAC_TISUBN (24 bits of sub-nanosecond increment)
If a one time adjustment is needed
  MAC_TA (30 bits of nanoseconds, plus a sign bit)

## Slide 39: LAN8650/1 Software
The TC6 driver software handles all features of the protocol
Set the FTSE (Frame Timestamp Enable) bit to provide timestamps on received packets.
Timestamps are delivered as part of the implementation. If enabled, they will be delivered in the payload structure.
They can be ignored by higher level packets unless they are explicitly needed
  The clock synchronization software will process PTP packets and pass the timestamps to the clock servo algorithm.

## Slide 40: Optional: Filter for SYNC Packets
Pattern for SYNC:
0x 88 F7 10
Configured in TXMPATH
(TX Match Pattern High)
Configured in TXMPATL
(TX Match Pattern Low)
Pattern Matcher can
check 3 Bytes
in RT/TX Ethernet frame
In case of a match
either RXPI, TXPI or RXTXPI pin is asserted
according to pin configuration
Arbitrary RX/TX Ethernet frame
Notes: The LAN86xx supports the implementation of PTP over Ethernet within the station controller by
being able to detect the exact time of transmission and reception of PTP messages. This is done by
examining the bytes of a packet that contain the EtherType and the first 2 bytes of the PTP header, and signaling when the correct pattern is detected.
To configure the desired pattern on transmitted packets, the most significant byte of the desired
value is written into the Transmit Match Pattern High (TXMPATH) register and the lower two octets of
the match value is written into the Transmit Match Pattern Low (TXMPATL) register. As an example,
to match on a SYNC message, the EtherType value of 0x88F7 and PTP header value of 0x10 creates
a 24-bit match value of 0x88F710. The value 0x88 is written into TXMPATH and the value 0xF710 is
written into TXMPATL.
Configuring the receive pattern matcher is done in a similar manner but using Receive Match Pattern High (RXMPATH) register and Receive Match Pattern Low (RXMPATL) register.
Pattern match output pins can be used on both transmitted and received packets.

## Slide 41: LAN8670/1/2 Timestamping
PTP relies on exact timestamps (Ts) broadcasted regularly (e.g. every 125 ms) in SYNC or FOLLOWUP messages by the Clock Source. All Clock Followers use this exact timestamp Ts to calculate the offset to their own time Ts.
Receiving a SYNC message (or any frame) is done without PLCA buffer, adding only internal fixed delays of PHY, MAC and stacks. Similar to LAN8650 except that there is no SPI protocol
Sending a SYNC message over a PLCA-based network adds a variable delay of 0-40 µs caused by the PLCA sending buffer when waiting for the own transmit opportunity and leads to an outdated timestamp Ts.
LAN8670/1/2 has two operational modes to solve this problem:
MCU
MAC
PHY
PLCA
PLCA Buffer
PCS
PMA
MII
MII
Transmit Match Enable
PHY recognizes an ingress/egress SYNC at its MDI
PHY informs MCU via GPIO
MCU can now compensate any delay in its time stamps due to PLCA or internal reasons (e.g. By using FOLLOW-UP messages)
MAC Transmit Time Stamp Enable
PHY signals a logical collision to the MAC when it starts sending a SYNC.
MAC will backoff and retry the SYNC with an updated timestamp Ts.
This retry will pass the PHY without PLCA buffer, i.e. having an exact timestamp.
GPIO
FOLLOWUP(Ts)
SYNC
Timestamp at MDI
MCU/
MAC
PHY
10BASE-T1S

## Slide 42: IEEE 802.1AS – Clock Synchronization (Standard)
In the clock source: Delays in PHY and because of PLCA lead to incorrect timestamp (generated by MCU) in SYNC
SYNC used “only” to trigger Pattern Matcher in LAN8670/1/2
MCU can now generate exact timestamp when SYNC has been sent out
Exact timestamp (of the previous SYNC) sent by subsequent FOLLOWUP
 Two-step-approach (Standard)
Clock
Source
Clock
Follower
SYNC()
SYNC()
FOLLOWUP()
FOLLOWUP ()
Pattern Matcher
PLCA
MCU
1.SYNC
3.FOLLOW-UP
1a.TXPI
2.

## Slide 43: IEEE 802.1AS – LAN8670/1/2 Configuration for Standard Clocksynchronization
Configure Pattern Matcher to detect TX SYNC packets (or other PTP message)
“Two-step-approach” (Standard)
TXME = 1 (Transmit Packet Match Enable)
in TXMCTL (Transmit Match Control Register)
In case of a match, the TXPI pin will be asserted to inform MCU.
MCU sends a FOLLOWUP, with previous TS
MACTXTSE and TXME cannot be set at the same time.
Functionalities mutually exclude each other.

## Slide 44: IEEE 802.1AS – Clock Synchronization (MAC Timestamping)
In the clock source:
Many MACs can capture their own transmit time stamps
However, TX PHY delay is variable (0...39,6 µs) because of PLCA elastic buffer
LAN8670/1/2 can be configured to make MAC Timestamping work
Patern Matcher detects TX-SYNC and triggers PLCA module
PLCA emulates collision to MAC
MAC terminates TX-SYNC and backs off
PLCA asserts Carrier Sense to keep MAC waiting until its next TO arrives
PLCA sends COMMITS to hold its TO
PLCA releases Carrier Sense
MAC retransmits SYNC with no delay
Clock Source
Clock Follower
SYNC()
previous
SYNC()
3.aborted
Pattern Matcher
PLCA
MAC
1.SYNC()
Buffer
2.COL
4.CRS
7.SYNC
(updated Ts)
5.COMMIT
SYNC()
7.retransmitted
trigger
6.release
FOLLOWUP ()

## Slide 45: LAN8670/1/2 Configuration for MAC Timestamping
In case of a match, the PLCA module will be triggered to
signal a logical collision to the MAC,
CRS is asserted until the next TO arrives,
and retransmitted SYNC can bypass the PLCA buffer.
“One-step-approach”
MACTXTSE =1
(MAC TX Time Stamp Enable)
Configure Pattern Matcher
to detect TX SYNC packets
(or other PTP message)

## Slide 46: Agenda
LAN8670/1/2 and LAN8650/1 Review
Features to Tune Bandwidth
Supporting Time Sensitive Networking
Wake/Sleep

## Slide 47: Wake / Sleep
Sleep mode
  Ultra low power consumption (<= 140 μW)
  Just constant 3.3V power supply during sleep, but no switched power
  Go to sleep via command from host
Wake from...
  Remote network Wake-Up Tone (WUT) (MDI)
  Local event (WAKE_IN), e.g. user input
Activate switched power
  INH pin output to enable/disable power supply
Forward wake signal
  Via WAKE_OUT to wake other local devices
  Via WAKE_OUT to inform MCU that network re-assumed operation
  Via activity* on MDI to wake other devices
As required in TC 10: Enables Wake/Sleep on small MCUs without external components
*LAN8670/1/1 Rev C and LAN8650/1 Rev B: MDI wake signal and detection does not meet the OPEN Alliance 10BASE-T1S Sleep/Wake-up Specification, version 1.0.
Device will wake on any activity on MDI, not just Wakeup-messages.
LAN8670/1/1 Rev D and LAN8650/1 Rev C: react only to Wake up Signal specified in OPEN Alliance 10BASE-T1S Sleep/Wake-up Specification, version 1.0
Notes: Note: In the LAN8670/1/2 and LAN8650/1 MDI wake detection was not designed to meet the OPEN Alliance
10BASE-T1S Sleep/Wake-up Specification, version 1.0. Received energy that is of sufficient length
that is detected either from other nodes transmitting onto the segment or from noise will trigger the
device to wake when MDI wake-up is enabled.

## Slide 48: Simple System without Sleep Mode
VDDA = power supply voltage for analog parts of the chip
VDDP = power supply voltage for digital parts of the chip
VDDAU = uninterruptible analog supply voltage
VSS = common ground exposed pad must be connected to the ground plane with a via array.
VDDAU only needed for wake detection in sleep mode
VDDA, VDDP, VDDAU
all connected to same
3.3V power supply
Since Sleep mode not used:
INH: no connect
WAKE_IN: connect to VSS
WAKE_OUT: No Connect

## Slide 49: System with Sleep Mode and Advanced Features
Wake-up might be forwarded via WAKE_OUT to local devices via MDI to wake remote nodes
VDDA, VDDP disabled in sleep mode VDDAU for wake-up detection
Wake-up can be forwarded via
WAKE_OUT to local devices
MDI to wake remote nodes
Wake-up is initiated by
the host via WAKE_IN,
network activity via MDI
After sleep mode starts, INH will be deasserted, which disables the voltage regulator for VDDA/VDDP
Notes: This slide shows an example of how power should be supplied in a system that will use the low-power sleep mode of the LAN8670/1/2 and LAN865/1. In this diagram, VDDAU is provided by a constant supply, so that it is always enabled, even during sleep mode. On system power-up, once this supply is active, the INH pin will be asserted so that its active high output can drive the enable pins of the external switchable supplies for VDDA and VDDP.
After the device enters sleep mode, the INH pin will enter a high-impedance state. The external resistor will pull the signal down to ground, which will then disable any voltage sources controlled by INH. This can be used to disable power to additional devices, including, when needed, the station controller.
The sleep/wake module is powered by the externally protected continuous VDDAU supply and detects a wake condition when the device is in the SLEEP state. This module monitors activity energy on the MDI interface and/or wake pulses on the WAKE_IN pin to determine if the device has received wake-up signaling. Once wake-up signaling has been received and validated, this module will drive the INH pin high to the VDDAU supply to enable the external switched power supplies.
If wake from the WAKE_IN pin is enabled (WKIEN=1), the WAKE_IN pin must be deasserted before the Sleep Inhibit Delay timer will be started.
Wake from MDI is enabled by writing a ’1’ to the MDI Wake Enable (MDIWKEN) bit in the Sleep
Control 0 (SLPCTL0) register prior to entering the SLEEP state.
The device may be configured to generate activity signaling on the MDI upon wake from SLEEP due to a wake pulse on WAKE_IN. The wake signaling consists of a 1 ms transmission of differential Manchester encoded pseudo-random binary data. The device will not listen for activity on the network prior to transmitting the wake signaling.
Enabling of MDI wake activity forwarding is accomplished by setting the MDI Forward Enable
(MDIFWDEN) bit of the Sleep Control 1 (SLPCTL1) register.
The WAKE_OUT pin may be configured to assert for 90 μs upon wake from SLEEP due to MDI activity or a wake pulse on WAKE_IN. Enabling of WAKE_OUT pin forwarding is accomplished by setting the WAKE_OUT Forward Enable (WKOFWDEN) bit of the Sleep Control 1 (SLPCTL1) register prior to entering the SLEEP state.

## Slide 50: Host Configures Each Time before Going to SLEEP...
Should other network nodes / local devices also be woken up by...
MDIFWDEN (MDI Forward Enable)
WKOFWDEN (WAKE_OUT Forward Enable)
Time from init SLEEP to INH release (leading to power off):
SLPINHDLY (Sleep Inhibit Delay)
Select wake-modes for next wake-up:
MDIWKEN (MDI Wakeup Enable)
WKINEN (WAKE_IN Enable)
Notes: Before entering SLEEP mode, the desired wake configuration must be
configured in the LAN8670/1/2 and LAN8650/1. It is recommended that this mode is configured
immediately after a reset.
Some systems may require a delay between the trigger for the start of sleep mode and disable
of the local power supplies, for example, to allow for other nodes on the mixing segment to go
quiet. Delay timing is configured with the Sleep Inhibit Delay (SLPINHDLY) field of the Sleep Control
0 (SLPCTL0) register.

## Slide 51: Current Wake/Sleep
LAN8670/1/2 Rev C
LAN8650/1 Rev B

## Slide 52: Going to SLEEP – Two Ways
Host actively sets
SLPEN (Sleep Enable) = 1
LAN865x or LAN867x waits for SLPINHDLY
(Sleep Inhibit Delay)
LAN865x or LAN867x automatically goes to SLEEP
when Watchdog timeout occurs
Host must configure 1...3 inactivity WD sources
No RX from network: MIRXWDEN (Media Interface Receive Watchdog Enable)
No TX to network: MITXWDEN (Media Interface Transmit Watchdog Enable)
No SMI access: PRIWDEN (PHY Register Inactivity Watchdog Enable )
configure IWDTOH / IWDTOH (Inact. WD Timeout)
unmask IRQ_N: IWDTOM = 0
set IWDE = 1 (Inactivity WD Enable)
In case of any timeout LAN865x or LAN867x
sets IWDTO = 1 (Inactivity WD Timeout Status)
waits for SLPINHDLY, and releases INH pin
LAN865x or LAN867x releases INH pin
ACTIVE
SLEEP
Power supplies MUST
turn off
Notes: After wake-up has been configured, the device may at any time be commanded to enter the SLEEP
state. This may be done in one of two ways. The station controller may initiate a transition to SLEEP
by writing a ‘1’ to the Sleep Enable (SLPEN) bit in the Sleep Control 0 (SLPCTL0) register. Alternatively,
the device may be configured to enter SLEEP automatically upon expiration of an inactivity watchdog.
The inactivity watchdog can be configured to trigger on inactivity of three sources: no receive
packets from the network, no transmit packets from the MAC, and no SMI access by the controller.
Each of these three inactivity sources may be enabled separately or together in any combination.
Once enabled, the watchdog timer will be reset upon detected activity on any of the selected
watchdog sources. When the watchdog expires, the Inactivity Watchdog Timeout (IWDTO) bit in
the Status 2 (STS2) register will be set commanding the transition to the SLEEP state and initiating
the Sleep Inhibit Delay timer.

## Slide 53: Wake – Sleep Cycle
ACTIVE
SLEEP
VDDA/P/U = ON,
INH = 1
Inactivity watchdog timeout or
app sets SLPEN (Sleep Enable) = 1
Wait for SLPINHDLY (Sleep Inhibit Delay)
Then release INH pin.
Power supplies turn off
Device in SLEEP
VDDAU = ON,
INH = 0
WAKE_IN asserted or
any activity detected on MDI
Drive INH = 1
VDDA/P/U = ON
if WAKEIND (Wake Indication) = 1,
set CLRWKI (clear wake indication) = 1
to activate wake-detection for the next wake-up
Check if WAKEIND (Wake Indication) = 1,
in case of a wake event:
check WKEWI (wake over Wake IN),
check WKEMDI (wake over MDI)

## Slide 54: New Wake/Sleep
LAN8670/1/2 Rev D
LAN8650/1 Rev C

## Slide 55: Going to SLEEP – Only One Way
Host actively sets
SLPEN (Sleep Enable) = 1
LAN865x or LAN867x waits for SLPINHDLY
(Sleep Inhibit Delay)
LAN865x or LAN867x releases INH pin
ACTIVE
SLEEP
Notes: After wake-up has been configured, the device may at any time be commanded to enter the SLEEP
state. This may be done in one of two ways. The station controller may initiate a transition to SLEEP
by writing a ‘1’ to the Sleep Enable (SLPEN) bit in the Sleep Control 0 (SLPCTL0) register. Alternatively,
the device may be configured to enter SLEEP automatically upon expiration of an inactivity watchdog.
The inactivity watchdog can be configured to trigger on inactivity of three sources: no receive
packets from the network, no transmit packets from the MAC, and no SMI access by the controller.
Each of these three inactivity sources may be enabled separately or together in any combination.
Once enabled, the watchdog timer will be reset upon detected activity on any of the selected
watchdog sources. When the watchdog expires, the Inactivity Watchdog Timeout (IWDTO) bit in
the Status 2 (STS2) register will be set commanding the transition to the SLEEP state and initiating
the Sleep Inhibit Delay timer.

## Slide 56: Wake – Sleep Cycle
ACTIVE
SLEEP
VDDA/P/U = ON,
INH = 1
App sets LPREQ bit in WS_CTRL register.
Wait for SLPINHDLY (Sleep Inhibit Delay)
Then release INH pin
Device in SLEEP
VDDAU = ON,
INH = 0
Wake event occurred,
Drive INH = 1
VDDA/P/U = ON
Exact indicators will match standard.
Vendor specific registers are not yet defined.
Lowest power only
when supplies off

## Slide 57: Current vs New Wake/Sleep
LAN8670/1/2 Rev D
LAN8650/1 Rev C

## Slide 58: Sleep – Direct Comparison
Current
New
Host actively sets SLPEN (Sleep Enable) = 1
Host can activate inactivity watchdog
  No RX from Network
  No TX to Network
  No PHY/SMI Register Access
Device waits for SLPINHDLY (Sleep Inhibit Delay)
Device releases INH pin
Host actively sets lpreq = 1 in WS_CTRL register
  New register required by OA Spec
Device waits for SLPINHDLY (Sleep Inhibit Delay)
Device releases INH pin

## Slide 59: Wake – Direct Comparison
Current
New
Network activity on MDI
External Controller via WAKE_IN
Wake Forwarding:
  External Controller/PHY on WAKE_OUT
  Network via MDI activity
Wake-Up Tone on MDI
External Controller via WAKE_IN
Wake Forwarding:
  External Controller/PHY on WAKE_OUT
  Network via MDI Wake-Up Tone

## Slide 60: Agenda

## Slide 61: PoDL – Power over Data Line
PoDL for multidrop networks is not specified in IEEE802.3cg, but only for 10BASE-T1L and 10BASE-T1S point-to-point
Number of nodes, stub length, bus length consume margin of signal integrity and robustness (incl EMC/EMI)
PoDL would be an engineered system, customer is in charge.

## Slide 62: PoDL Power Sourcing Equipment (PSE) – Internal Test Boards Only
Display shows current power
PoDL output power
4 - 24V / max 1600 mA
Configurable via jumpers
10BASE-T1S interface
10BASE-T1S bus termination via jumpers

## Slide 63: PoDL Powered Device (PD) – Internal Test Boards Only
PoDL Board AIS20040
3.3V / 150 mA LDO
3.3V / 500 mA switched power,
Bus termination via jumpers
LAN8651 node AIS20039
mikroBUS™ clickboard™
5V / 500 mA optional
Voltage regulation via jumpers
Curiosity Nano Base Board
SAMD21 Curiosity Nano Microcontroller board

## Slide 65: Thanks for your time!
Do you have any questions?